## Slide 1
Cabinet details
Standard
Comply with ANSI/EIA RS-310-D, DIN41497 part 1, IEC297-2, DIN41494 part 7, GBIT3047.2-92 standard.
Feature
19 inch standard;
Removable Side Panels, side locks optional;
Knock off hole for entering cable on both top cover, bottom panel,real panel
Turning angle of front door is over 180 degrees
Easy mounting installation
Unassembled package saving shipping space
fans, shelf, PDU are optional
Loading Capacity
60KG
Degree of Protection
IP20
Material
SPCC Cold Rolled Steel
Thickness:1.0mm-0.8mm-0.6mm
Surface Finish:
Powder coating
Removable side panels
(Side lock optional)
Cable entrance on rear panel
Zinc plated mounting profile with U mark
(Ground wire optional)
Front tempered glass door
Bottom
Fan exhaust hole
WB Single Section Wall Mounted Cabinets

## Slide 2
Front view
(Toughened glass)
Side view
Back view
Top view
Inside view
Main dimension 9U 600*450*501mm
WB Single Section Wall Mounted Cabinets
bottom

## Slide 3
S/N | Specification | Quantity | Unit | Material | Surface Finish | Remark
1 | Mounting profile | 4 | Piece | Coated Zinc plate t1.0 | Coated Zinc | with U mark
2 | Frame | 2 | Piece | SPCC cold rolled steel t0.8 | Powder coated | 
3 | Side panel | 2 | Piece | SPCC cold rolled steel t0.6 | Powder coated | 
4 | Top cover | 1 | Piece | SPCC cold rolled steel t0.6 | Powder coated | 
5 | Bottom panel | 1 | Piece | SPCC cold rolled steel t0.6 | Powder coated | 
6 | Rear panel | 1 | Piece | SPCC cold rolled steel t0.6 | Powder coated | 
7 | Front door | 1 | Piece | 5MM toughened glass door/SPCC t0.8 | Powder coated | 
8 | Lock | 1 | Piece | Steel | Color Zinc | with 2 keys
9 | M6 Square nut | 12 | Piece | Steel | Color Zinc | 
10 | M6 B-head screw | 12 | Piece | Steel | Color Zinc | 
11 | Allen wrench | 1 | Piece | Steel | Color Zinc | 
Model No. | Capacity | Width | Depth | Height | Packing dimension | Volume
 | (U) | (mm) | (mm) | (mm) | (mm) | (CBM)
WB.6404 | 4 | 600 | 450 | 280 | 635*485*160 | 0.049
WB.6604 |  |  | 600 |  | 635*635*230 | 0.093
WB.6406 | 6 | 600 | 450 | 368 | 635*485*160 | 0.049
WB.6606 |  |  | 600 |  | 635*635*230 | 0.093
WB.6409 | 9 | 600 | 450 | 501 | 635*485*235 | 0.072
WB.6609 |  |  | 600 |  | 635*635*231 | 0.093
WB.6412 | 12 | 600 | 450 | 635 | 665*595*236 | 0.093
WB.6612 |  |  | 600 |  | 665*635*231 | 0.098
RAL9004 | RAL7035
black | grey
WB Single Section Wall Mounted Cabinets
Specification
Main Parts
Color